## Slide 2: Don’t Open Row: Rethinking Row Buffer Policy for Improving Performance of Non-Volatile Memories
Yongho Lee, Osang Kwon and Seokin Hong

## Slide 3: Background

## Slide 4: PCM (Phase Change Memory)
Non-volatile
High capacity
Low power
Possible DRAM replacement
Background
Intel Optane DC Persistent Memory Module1
1Brian Beeler, StorageReview, April 2, 2019

## Slide 5: PCM (Phase Change Memory)
RESET(bit ‘0’) : Short duration, High electrical pulse
SET(bit ‘1’) : Long duration, Low electrical pulse
The speed of the write operation is much slower than that of the read operation
Background

## Slide 6: PCM Architecture & Operations
Read Operation
Background
row-decoder
row-addr
row-buffer
wordline
bitline
Row-Data
row activate
write-driver
row-decoder
row-buffer
Data
1. Activation
2. Read
Chip

## Slide 7: PCM Architecture & Operations
Write Operation
Background
row-decoder
row-addr
row-buffer
wordline
bitline
Row-Data
row activate
write-driver
row-decoder
row-buffer
Data
1. Activation
2. Write
write-driver
Chip

## Slide 8: Major Hurdle: Slow PCM Operations
Row activation latency (tRCD) and Write latency (tWR) are much longer than others
Background
RD
PRE
ACT
ACT
Read
WR
PRE
ACT
ACT
Write
tRCD
tRCD
tBURST + tWR
Row activation and write operation are major bottlenecks limiting the performance of PCM systems
tRCD
tBURST + tWR
tRCD

## Slide 9: Row Buffer Policy
Open-page Policy
  Keeps the row data in the row buffer until another row is activated (i.e., bank conflict occurs)
Close-page Policy
  Closes the activated row immediately after the subsequent read or write request is serviced on the activated row
Background
Both policies cannot hide the long activation latency if the row buffer locality is low

## Slide 10: Write Scheme
Write-Back
  Data is only written to the row buffer, then written back to PCM cells when closing the open row
   Fast writes on row buffer hit
  When a bank conflict occurs, the data in the row buffer has to be written back to PCM cells
   High bank conflict overhead
Background
row-decoder
row-addr
row-buffer
open row
write-driver
row-decoder
row-buffer
Data
write-driver

## Slide 11: Write Scheme
Background
Both policies require the slow row activation
row-decoder
row-addr
row-buffer
open row
write-driver
row-decoder
row-buffer
Data
write-driver
Write-Through
  Data is written to both row buffer and PCM cells at the same time
  When a bank conflict occurs, the open row can be immediately closed
   Low bank conflict overhead

## Slide 12
Problem:
Row activation latency is a major bottleneck in PCM systems
Limitation of Current Mechanisms:
Conventional row buffer policies and write schemes cannot address this problem.
Our goal: Mitigating slow row activation in PCM systems

## Slide 13: Motivation

## Slide 14: Poor Locality of Write Requests
Average row-buffer hit rate of read requests : 32%
Average row-buffer hit rate of write requests : 1%
Motivation
The write requests have poor row buffer locality

## Slide 15: Non-destructive ACT in PCM
Row activation destroys data stored in the DRAM cells
To restore destructed data, the activated row should be latched by the sense amplifier(row buffer)
Plate
Wordline
Capacitor
Bitline
S/A
DRAM
Motivation
Destroyed!
Restored!

## Slide 16: Non-destructive ACT in PCM
Row activation does not destroy data stored in the PCM cells
Latching activated row in row buffer is not necessary
Bitline
Wordline
Resistive
Storage
1Lu, Shyue-Kung, et al., Journal of Electronic Testing 37.4, 2021
PCM1
Motivation
Not Destroyed!
Plate
Wordline
Capacitor
Bitline
S/A
DRAM
Restored!

## Slide 17: Non-destructive ACT in PCM
Non-destructive property enables the separation of the row activation operation into two sub-operations in the PCM systems:
1Lu, Shyue-Kung, et al., Journal of Electronic Testing 37.4, 2021
Motivation
Plate
Wordline
Capacitor
Bitline
DRAM
Bitline
Wordline
Resistive
Storage
PCM1
row-decoder
row-addr
row-buffer
wordline
bitline
Data
fetching data
Decoding row address
+ Fetching data to the row buffer

## Slide 18: Write-Around PCM System

## Slide 19: Key Idea
Write-Around PCM system does not fetch data to the row buffer for write requests
Instead, it only drives a wordline to connect PCM cells in the target row to bitlines
When a write request is issued, the given data is directly written to the PCM cells
Write-Around PCM System
To apply Write-Around scheme to the PCM systems,
we propose Pseudo Row Activation and Direct Write

## Slide 20: Pseudo Row Activation
Conventional row activation (ACT)
  The entire PCM cells of the target row are connected to bitlines
  Fetch the data stored in the target row into the row buffer
  Fetching the data accounts for the majority of row activation latency.
Write-Around PCM System
row-decoder
row-addr
row-buffer
wordline
bitline
Data
row activate
7.5ns(13%)
48ns(87%)
open row

## Slide 21: Pseudo Row Activation
Pseudo row activation (P-ACT)
  Does not fetch the data stored in the target row
  Just drives the wordline of the target row
  P-ACT reduces the row activation latency by 87%
Write-Around PCM System
row-decoder
row-buffer
row activate
bitline
row-addr
wordline
pseudo-
open row
7.5ns(13%)

## Slide 22: Direct Write
Writes data directly to the pseudo-open row
  PCM cells of the pseudo-open row are connected to the bitlines
  So, data can be written directly to the pseudo-open row by injecting proper write pulses to the bitlines
Write-Around PCM System
row-decoder
wordline
direct write
bitline
row-addr
data
75ns
write driver
row-buffer
write driver

## Slide 23: Write-Around PCM system
Write-Back : tRCD + tBURST + tWR + tRP + tRCD
Write-Around : tPRCD + tBURST + tWR + tRP + tRCD
tPRCD is much shorter than tRCD
Write-Around PCM System
speedup
tPRCD
tBURST + tWR
WR
PRE
P-ACT
ACT
tRP
tRCD
RD
tRCD
WR
PRE
ACT
ACT
RD
tRP
tRCD
Write-Around
Write-Back
tBURST + tWR
RD
RD

## Slide 24: Implementation
The PCM controller for Write-Around PCM systems
  1. issues Pre-ACT command first when activating a row
  2. then sends ACT command
Pre-ACT can be encoded by using the RFU (Reserved for future use) slot existing in the DDR4 or DDR5 specification
Write-Around PCM System
Clock
Addr
Cmd
Data
tCMD
D1
D3
D2
D4
D6
D5
D8
D7
ACT
Bank
PRE
tPRCD
tBURST + tWR
WR
Col
Row
tWL
Pre-ACT
P-ACT

## Slide 25: Evaluation

## Slide 26: Evaluation Methodology
Simulation infrastructure
  GEM5
  NVMain
Benchmark
  SPEC CPU 2006
Competitive techniques
  WB-PCM, WT-PCM
Component | Configuration
Processor | 3GHz, x86 4Cores
Caches | L1 : I/D 32KB, 8 way, 4-cycle, private L2 : 4MB, 16way, 12-cycle, shared
Memory controller | FR-FCFS, 32 entries queue, Open page policy (for baseline) Pseudo-open page policy (for Ours)
Main memory | 400 MHz, 8GB, 2KB buffer, 1 channels, 2 rank / channels, 8 bank / rank
Memory timing parameters | tRCD 60ns, tWR 75ns, tCWD 10ns, tPRCD 10ns
Evaluation

## Slide 27: Performance Result
Average speedup of 15% over the WB-PCM, 4% over the WT-PCM
For 12 of 23 workloads, 24% over the WB-PCM, 7% over the WT-PCM
Evaluation

## Slide 28: Energy Result
WA-PCM consumes 41% less energy than WB-PCM
For 12 of 23 workloads, consumes 47% less energy on average
Similar energy consumption to WT-PCM
Evaluation

## Slide 29: Conclusion
The demands for scalable memory systems are increasing
  PCM systems have attracted significant attention as an alternative to DRAM
  But, the performance of PCM systems is still much lower than DRAM
Write-Around PCM system  Reduces the row activation latency
  Pseudo Row Activation + Direct Write
15% Performance gain over the WB-PCM (4% over the WT-PCM)
41% Energy reductions over the WB-PCM (similar to the WT-PCM)

## Slide 30: Thank You