## Slide 1: Conveyor: Towards Asynchronous Dataflow in Systolic Array to Exploit Unstructured Sparsity
Seongwook Kim, Gwangeun Byeon, Sihyung Kim, Hyungjin Kim, Seokin Hong
Department of Electrical and Computer Engineering,
Sungkyunkwan University,
Suwon, Korea
Presenter: Seongwook Kim

## Slide 2: Contents
Background
  Sparsity Exploitation
  Limitations of Conventional Sparse-DNN Accelerators
  PE Underutilization Issue
Motivation
  Chunk Propagation and Load Imbalance
  Asynchronous Dataflow in Systolic Array
  Operand Queue
Conveyor-SA Architecture
  What is Conveyor Queue?
  Asynchronous Dataflow with Conveyor Queue
  Conveyor-SA Architecture
Evaluation
  Methodology
  Performance Evaluation
  Hardware Overhead
Conclusion

## Slide 3: Background

## Slide 4: Sparsity Exploitation
DL workloads show high sparsity
Zero values generate a large number of ineffectual computations
About 60% of the total computations are ineffectual
Ratio of effectual/ineffectual computations of CNN workloads

## Slide 5: Limitations of Conventional Sparse-DNN Accelerators
Systolic Array-like architecture
  Static Dataflow
  (+) Low hardware overhead
  (-) Hard to skip ineffectual computations
PE
PE
PE
PE
Activation Buffer
Weight Buffer
Nonzero
Zero
Accelerator with Flexible Networks
  Flexible Dataflow
  (+) Assigns only effectual computations
  (-) High hardware overhead
Unified Buffer
PE
PE
PE
PE
Distribution
Network
Reduction
Network

## Slide 6: PE Underutilization Issue
Systolic Array has static dataflow  Zero values needs to be propagated
PE Underutilization: PEs with zero values must be underutilized
About 55% of the PEs are underutilized
PE underutilization of Systolic Array architectures

## Slide 7: Motivation

## Slide 8: Chunk Propagation and Load Imbalance Issue
Propagate data chunks through the PE array instead of a single value
PE extracts valid operand pairs from the data chunks  Sparsity Exploitation
Speed differences between adjacent PEs  Load Imbalance
3 valid operand pairs = 3 computation cycles
cycle 1
cycle 2
cycle 3
activation
chunk
8
0
2
4
0
0
7
0
weight
chunk
5
3
4
0
0
3
2
6
pair 0
pair 1
pair 2

## Slide 9: Asynchronous Dataflow in Systolic Array
Synchronous  Fast PE waits until slow neighbor finishes current task
Asynchronous  Fast PE can move on to the next task right after it finishes its current task
Asynchronous dataflow relieves PE underutilization caused by the load imbalance issue
PE
PE
fast
stall
slow
PE
slow
stall
Sync. Dataflow
PE
PE
fast
slow
PE
slow
Async. Dataflow

## Slide 10: Operand Queue
Operand Queue: FIFO buffer between the adjacent PEs
  (+) Fast PE can transfer data to the Operand Queue even though the succeeding PE is still busy
  (-) Ineffective for slow-fast relationship scenario
  (-) Huge hardware overhead
Scenario 1: fast-slow relationship
PE
(consumer)
Operand Queue
data
fast
slow
data
PE
(producer)
Scenario 2: slow-fast relationship
PE
(consumer)
Operand Queue
slow
fast
PE
(producer)
stall

## Slide 11: Conveyor-SA Architecture

## Slide 12: What is Conveyor Queue?
Search Window
used workloads
unused workloads
Conveyor Belt
Search Window
used data chunk
unused data chunk
Conveyor Queue
PE
PE
PE
Conveyor Queue distributes data chunks to the PEs
PE dynamically selects unused data chunk from its own search window
PE does not directly transfer data chunk to the adjacent PE
Conveyor Queue propagates data only if all the PEs are having data chunks to be transferred

## Slide 13: Asynchronous Dataflow with Conveyor Queue
chunk 4
PE
PE
chunk 3
chunk 2
chunk 3
chunk 2
Each PE independently fetches data chunk from its own search window
Search window of adjacent PEs are overlapping with each other
Conveyor Queue
chunk 5
chunk 6
chunk 4
chunk 2
chunk 3
chunk 1
chunk 0
chunk 5
chunk 4
chunk 2
chunk 4
chunk 3
chunk 1
shared
region
search window
search window
fast
slow

## Slide 14: Asynchronous Dataflow with Conveyor Queue
chunk 3
PE
PE
chunk 3
chunk 2
Each PE independently fetches data chunk from its own search window
Search window of adjacent PEs are overlapping with each other
Conveyor Queue
chunk 5
chunk 6
chunk 4
chunk 2
chunk 3
chunk 1
chunk 0
chunk 5
chunk 4
chunk 2
chunk 4
chunk 3
chunk 1
shared
region
search window
search window
slow
fast
chunk 3
chunk 2
Conveyor Queue provides asynchronous dataflow

## Slide 15: Conveyor-SA Architecture
2D pipeline is replaced with a mesh composed of Conveyor Queues
SPU (Synchronous Processing Unit): Cluster of PEs sharing the same data chunks
Weight and activation data are propagated through the Conveyor Queue
SPU dynamically selects data chunk from its own search window

## Slide 16: Conveyor-SA Architecture
chunk group 0
Conveyor Controller
request
response
chunk group 5
chunk group 4
chunk group 3
chunk group 2
chunk group 1
SPU
Conveyor Queue
Read pointer (red arrow) is directed towards the data chunk currently being used
Read pointer indicates whether for the SPU to request a new data chunk
  Conveyor Controller propagates data chunks only if all the SPU requests new chunk
  Conveyor Controller send response to guarantee the read pointer is directed to the same data chunk
Conveyor Queue
SPU1
SPU2
SPU3
chunk group 0
chunk group 8
Conveyor Controller
shift trigger
SPU0
shift response
request
response
request
response
request
response
request
response
chunk group 7
chunk group 6
chunk group 5
chunk group 4
chunk group 3
chunk group 2
chunk group 1

## Slide 17: Evaluation

## Slide 18: Methodology
Baseline Architectures
  Conventional Systolic Array with Output Stationary Dataflow (SAOS)
  Systolic Array with Operand Queue (SMT-SA*)
Performance Evaluation
  Cycle-level simulator of Conveyor-SA
  Workloads: CNN Inference (quantized to INT8) – AlexNet, VGG16, ResNet18/34/50
Hardware Overhead
  RTL design of the Conveyor-SA
  Synopsys Design Compiler with UMC 28nm cell library
  CACTI 7.0 for assessing SRAM buffers
* Shomron, G., Horowitz, T., & Weiser, U. (2019). SMT-SA: Simultaneous multithreading in systolic arrays. IEEE Computer Architecture Letters, 18(2), 99-102.

## Slide 19: Performance Evaluation
Inference speedup of CNN models without weight pruning
  About 1.94x better performance than SAOS
  About 1.42x better performance than SMT-SA
Inference speedup of CNN models with 50% unstructured weight pruning
  About 2.09x better performance than SAOS
  About 1.46x better performance than SMT-SA
Without weight pruning
With 50% unstructured weight pruning

## Slide 20: Hardware Overhead
Hardware Configuration
 | SMT-SA | Conveyor-SA
Total Number of SPU | 1024 (32x32) | 64 (8x8)
PEs per SPU | 1 (1x1) | 16 (4x4)
Total Number of PEs | 1024 | 
Chunk Size | 8 | 
Window Size | 4 | 
Buffer Configuration | 2MB (Activation Buffer), 0.5MB (Weight Buffer) | 
Analysis on Area and Power Consumption
 | SMT-SA |  | Conveyor-SA | 
 | Area | Power | Area | Power
Activation Buffer | 54.59% | 58.40% | 67.87% | 76.34%
Weight Buffer | 14.76% | 14.16% | 18.35% | 18.51%
Operand Queue / Conveyor Queue | 22.86% | 24.00% | 4.49% | 1.60%
PE | 7.79% | 3.44% | 9.29% | 3.55%
Total | 4.20 mm2 | 1060.27 mW | 3.38 mm2 | 811.11 mW

## Slide 21: Conclusion

## Slide 22: Conclusion
DL workloads have high sparsity
It is important to skip ineffectual computations
The load imbalance between PEs causes PE underutilization of Sparse-SA architectures
Conveyor-SA Architecture
  Conveyor Queue to provide asynchronous dataflow to the PE array
Evaluation
  About 2x better performance than conventional systolic array
  About 1.4x better performance than systolic array with operand queues
  Conveyor Queue shows lower hardware overhead than Operand Queue

## Slide 23: Thank You !

## Slide 24: Operand Queue
What is Operand Queue?
  Insert queue based buffer between the adjacent PEs
  Fast PE transfers and receives data to and from the queue
  Only effective for fast-slow relationship scenario
Scenario 1: fast-slow relationship
Scenario 2: slow-fast relationship

## Slide 25: Limitation of Operand Queues
Large Hardware Overhead of Operand Queues
  Estimate the number of registers that the Operand Queue takes with respect to the size of PE array
  Operand Queue requires large number of registers
  Operand Queues take large chip area and power consumption

## Slide 26: Synchronous Processing Unit
DL workloads have wide range of sparsity
It takes time to propagate dense data chunks through the Conveyor Queue
Need to improve performance for the dense workloads by reducing the propagation delay
Synchronous Processing Unit (SPU): cluster of PE sharing the same data chunk
Decrease the propagation delay of the dense data chunks by factor of the SPU dimension
Weight Chunk Group
Activation Chunk Group

## Slide 27: Asynchronous Dataflow with Conveyor Queue
Each PE independently fetches data chunk from its own search window
Search window of adjacent PEs are overlapping with each other
Conveyor Queue alleviates PE underutilization caused by the load imbalance issue
  fast-slow relationship: shared region provides virtual FIFO between PEs
  slow-fast relationship: shared region provides virtual handshake between PEs

## Slide 28: Conveyor-SA Architecture
Read pointer (red arrow) is directed towards the data chunk currently being used
SPU fetches data chunk independently from the Conveyor Queue using read pointer
  If the read pointer points to the end of the search window, Conveyor Queue doesn’t shift the data chunks
  If not, Conveyor Queue shifts the data chunks and send response signal to the SPUs
  SPU increases read pointer to make sure that the read pointer is directed to the same data chunk
Weight Conveyor Queue
SPU1
SPU2
SPU3
chunk group 0
chunk group 8
Conveyor Controller
shift trigger
SPU0
shift response
request
response
request
response
request
response
request
response
chunk group 7
chunk group 6
chunk group 5
chunk group 4
chunk group 3
chunk group 2
chunk group 1