## Slide 1: Rethinking Page Table Structure for Fast Address Translation in GPUs: A Fixed-Size Hashed Page Table
Sungbin Jang, Junhyeok Park, Osang Kwon, Yongho Lee, and Seokin Hong
Sungkyunkwan University
PACT '24: International Conference on Parallel Architectures and Compilation Techniques
Notes: Good morning, everyone.
My name is Sungbin Jang.
I’m a Ph.D. student at Sungkyunkwan University, South Korea.
Now, I’ll talk about our research paper, Rethinking Page Table Structure for Fast Address Translation in GPUs: A Fixed-Size Hashed Page Table.

## Slide 2: Heterogeneous Computing Systems
GPUs have become common device for heterogeneous computing.
1
Notes: GPUs have become essential for heterogeneous computing for accelerating various types of applications such as graph processing, large language model, and so on.

## Slide 3: Traditional GPU Programming Model
Traditional copy-then execute model needs a complicated data management.
2
PCIe
CPU Memory
GPU Memory
Notes: In traditional systems, the CPU and GPU have a separate address space.
Therefore, if the GPU wants to access data in the CPU side, a programmer has to manually copy data from the CPU to GPU.

## Slide 4: GPU Memory Virtualization
Virtual memory systems have become essential for GPUs.
  Ease GPU programming with a unified address space.
  Enable GPU to handle large data sets beyond GPU’s local memory size.
Programmer transparent memory management
3
PCIe
Unified Virtual Address Space
Notes: With advent of the GPU memory virtualization, GPU and CPU share a single unified memory space.
This feature eases GPU programming and enable GPUs can deal with large datasets beyond its memory capacity.

## Slide 5: GPU Memory Virtualization
Virtual memory systems have become essential for GPUs.
  Ease GPU programming with a unified address space.
  Enable GPU to handle large data sets beyond GPU’s local memory size.
Programmer transparent memory management
3
PCIe
Unified Virtual Address Space
However, GPU memory virtualization does not come for free!
Notes: However, this memory virtualization does not come for free because of the address translation overhead!

## Slide 6: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Notes: The figure on the slide is a brief overview of the GPU virtual memory system.

## Slide 7: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Notes: Once the core issues memory related instructions, before accessing cache hierarchy,

## Slide 8: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Notes: GPU has to look up TLBs.

## Slide 9: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Notes: If there is no matching entry in TLBs, the translation request is forwarded to GPU MMU.

## Slide 10: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Notes: Then, page table walker starts page table access.

## Slide 11: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Notes: First, it looks up page walk caches to skip accessing some level of page table.

## Slide 12: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Notes: After that, the walker accesses each level of page tables sequentially,

## Slide 13: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
Sequential Memory Accesses
❶
❷
❸
❹
4
Notes: and finally gets the desired PA from the last level of page tables.

## Slide 14: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
Sequential Memory Accesses
❶
❷
❸
❹
4
Notes: and finally gets the desired PA from the last level of page tables.

## Slide 15: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Notes: Now, the GPU can access data pages using the derived PA.

## Slide 16: Address Translation in GPUs
L1 TLB
CUs
SMs
Shared L2 TLB
Page Table Walkers
GMMU
Page Walk Cache
Page Walk Queue
Device memory
Page Table
PML4
PT
PD
PDP
PTBR
Data
Pages
4
Address translation puts high pressure on the memory systems!
Notes: Such an address translation puts high pressure on the memory systems, causing a significant performance degradation.

## Slide 17: Radix Page Tables
Conventional GPUs adopt multi-level Radix Page Tables (RPTs).
5
* PTBR: Page Table Base Register
PML4 offset
Page offset
47:39
11:0
PT offset
20:12
PD offset
29:21
PDP offset
38:30
PML4E
+
PDPE
PTE
PDE
+
PTBR
+
+
PML4
PDP
PD
PT
VA
Notes: One of the key bottlenecks in address translation is page table access.
This is because conventional GPUs adopt multi-level Radix Page Table as their page table structure.

## Slide 18: Radix Page Tables: Limitations
RPTs require several sequential memory accesses per page table walk.
  For 4-level, up to four sequential memory accesses are required!
PML4 offset
Page offset
47:39
11:0
PT offset
20:12
PD offset
29:21
PDP offset
38:30
PML4E
+
PDPE
PTE
PDE
+
PTBR
+
+
PML4
PDP
PD
PT
VA
6
* PTBR: Page Table Base Register
Page Table Walker
Device Memory
Notes: This structure is spatially efficient, but it introduces sequential memory access overhead.

## Slide 19: Radix Page Tables: Limitations
RPTs require several sequential memory accesses per page table walk.
  For 4-level, up to four sequential memory accesses are required!
PML4 offset
Page offset
47:39
11:0
PT offset
20:12
PD offset
29:21
PDP offset
38:30
PML4E
+
PDPE
PTE
PDE
+
PTBR
+
+
PML4
PDP
PD
PT
VA
6
* PTBR: Page Table Base Register
Page Table Walker
Device Memory
Notes: For example, when the page table walker wants to get virtual-to-pyhsical mapping,

## Slide 20: Radix Page Tables: Limitations
RPTs require several sequential memory accesses per page table walk.
  For 4-level, up to four sequential memory accesses are required!
PML4 offset
Page offset
47:39
11:0
PT offset
20:12
PD offset
29:21
PDP offset
38:30
PML4E
+
PDPE
PTE
PDE
+
PTBR
+
+
PML4
PDP
PD
PT
VA
6
* PTBR: Page Table Base Register
Page Table Walker
Device Memory
Notes: it needs to access the cache hierarchy four times sequentially.

## Slide 21: Page Walk Caches
Page Walk Caches mitigates sequential access overhead of RPTs.
PML4 offset
Page offset
47:39
11:0
PT offset
20:12
PD offset
29:21
PDP offset
38:30
PML4E
+
PDPE
PTE
PDE
+
PTBR
+
+
PML4
PDP
PD
PT
VA
6
* PTBR: Page Table Base Register
Page Table Walker
Device Memory
Page Walk Cache
Notes: To mitigate this sequential access overhead, conventional GPUs are equipped with a PWC in the GMMU.
Since Page Walk Caches store the physical address of recently accessed page tables,

## Slide 22: Page Walk Caches
Page Walk Caches mitigates sequential access overhead of RPTs.
PML4 offset
Page offset
47:39
11:0
PT offset
20:12
PD offset
29:21
PDP offset
38:30
PML4E
+
PDPE
PTE
PDE
+
PTBR
+
+
PML4
PDP
PD
PT
VA
6
* PTBR: Page Table Base Register
Page Table Walker
Device Memory
Skip upper levels
Page Walk Cache
Notes: it allows the page table walker to skip accessing some level of page tables.

## Slide 23: Page Walk Caches
Page Walk Caches mitigates sequential access overhead of RPTs.
PML4 offset
Page offset
47:39
11:0
PT offset
20:12
PD offset
29:21
PDP offset
38:30
PML4E
+
PDPE
PTE
PDE
+
PTBR
+
+
PML4
PDP
PD
PT
VA
6
* PTBR: Page Table Base Register
Page Table Walker
Device Memory
Skip upper levels
Directly Access Last Level
Page Walk Cache
Notes: In the best case, with the PWCs the page table walker can access the last-level page table directly.

## Slide 24: Page Walk Caches: Limitations
However, PWCs show high miss rate for irregular workloads.
Chart: Miss Rate
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
Lv.2 PWC Miss Ratio | 0.41357 | 0.39234 | 0.42092 | 0.33146 | 0.2642 | 0.39359 | 0.21476 | 0.34316 | 0.33877 | 0.00197 | 0.00201 | 0.00196 | 0.03542 | 0.03734 | 0.0031 | 0.00199 | 0.00197 | 0.0043351
7
Notes: However, for irregular applications, PWCs show a high miss rate, causing sequential memory access overhead again.

## Slide 25: Page Walk Caches: Limitations
However, PWCs show high miss rate for irregular workloads.
  Irregular workloads shows low locality in data access.
Chart: Miss Rate
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
Lv.2 PWC Miss Ratio | 0.41357 | 0.39234 | 0.42092 | 0.33146 | 0.2642 | 0.39359 | 0.21476 | 0.34316 | 0.33877 | 0.00197 | 0.00201 | 0.00196 | 0.03542 | 0.03734 | 0.0031 | 0.00199 | 0.00197 | 0.0043351
33.8%
7
Notes: This is because the irregular workloads show low locality in data access.

## Slide 26: Page Walk Caches: Limitations
However, PWCs show high miss rate for irregular workloads.
  Irregular workloads shows low locality in data access.
Chart: Miss Rate
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
Lv.2 PWC Miss Ratio | 0.41357 | 0.39234 | 0.42092 | 0.33146 | 0.2642 | 0.39359 | 0.21476 | 0.34316 | 0.33877 | 0.00197 | 0.00201 | 0.00196 | 0.03542 | 0.03734 | 0.0031 | 0.00199 | 0.00197 | 0.0043351
33.8%
7
How can we remove this sequential access overhead?
Notes: Then, how can we remove this sequential access overhead of page table?

## Slide 27: Hashed Page Tables
Hashed Page Tables (HPTs) requires only a single memory access.
Page offset
11:0
VPN tag
47:12
PTBR
HPT
PTE
tag
VA
8
* PTBR: Page Table Base Register
Notes: One of the answers is using Hashed Page Tables.
Hashed Page Table stores the translation information in the contiguous region in the physical memory.

## Slide 28: Hashed Page Tables
Hashed Page Tables (HPTs) requires only a single memory access.
Page offset
11:0
VPN tag
47:12
PTBR
+
H
idx
HPT
PTE
tag
VA
8
* PTBR: Page Table Base Register
Notes: So, accessing Hashed Page Tables can be done simply by adding hash value of the VA with the page table base address.

## Slide 29: Motivational Study: Ideal HPT
Ideal HPT shows a substantial performance improvement.
Chart: Speedup
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
RPT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Ideal PWC | 1.3826 | 1.2913 | 1.3609 | 1.3338 | 1.1638 | 1.3678 | 1.1857 | 1.2604 | 1.2908 | 0.99839 | 1.0029 | 0.99935 | 1.0334 | 1.0203 | 1 | 1.0013 | 0.99949 | 1.0068
9
Notes: To see impact of HPT on the GPUs, we compare the RPT with the HPT.

## Slide 30: Motivational Study: Ideal HPT
Ideal HPT shows a substantial performance improvement.
Chart: Speedup
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
RPT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Ideal PWC | 1.3826 | 1.2913 | 1.3609 | 1.3338 | 1.1638 | 1.3678 | 1.1857 | 1.2604 | 1.2908 | 0.99839 | 1.0029 | 0.99935 | 1.0334 | 1.0203 | 1 | 1.0013 | 0.99949 | 1.0068
29%
9
HPT
Notes: The results show that HPT outperforms RPTs by 29% for irregular workloads.

## Slide 31: Hash Collisions
Handling hash collisions is one of the key challenges in applying HPTs.
HPT
PTE
0xF
10
Notes: Using HPTs seems to be a good choice.
However, to apply HPT, we have to handle a hash collision which is one of the key challenges in applying HPT.

## Slide 32: Hash Collisions
Handling hash collisions is one of the key challenges in applying HPTs.
HPT
PTE
0xF
10
VA 0
tag: 0xF
VA 1
tag: 0xA
Notes: Due to the inherent of hashing, two or more keys can be assigned to the same hash slot.

## Slide 33: Hash Collisions
Handling hash collisions is one of the key challenges in applying HPTs.
HPT
PTE
0xF
10
VA 0
tag: 0xF
VA 1
tag: 0xA
≠
Notes: In this example, if we access the hash table with a VA 1 with a tag A,

## Slide 34: Hash Collisions
Handling hash collisions is one of the key challenges in applying HPTs.
HPT
PTE
0xF
10
VA 0
tag: 0xF
VA 1
tag: 0xA
≠
Hash Collision!
Notes: the hash collisions occurs because VA 0 with tag F already occupies that slot.
Handling hash collisions requires additional penalties such as additional memory accesses.

## Slide 35: Occupancy
Occupancy is the percentage of entries populated in the hash table.
HPT
11
HPT
Notes: The probability of occurring hash collisions is tightly related to the occupancy of the hash table.

## Slide 36: Occupancy
Occupancy is the percentage of entries populated in the hash table.
HPT
11
HPT
Occupancy: 20%
Occupancy: 80%
Notes: The more occupancy,

## Slide 37: Occupancy
Occupancy is the percentage of entries populated in the hash table.
HPT
11
HPT
Occupancy: 20%
Occupancy: 80%
More likely to occur hash collisions!
Notes: the more probability of occurring hash collisions.

## Slide 38: Occupancy
Occupancy is the percentage of entries populated in the hash table.
HPT
11
HPT
Occupancy: 20%
Occupancy: 80%
More likely to occur hash collisions!
Keeping the occupancy low is important!
Notes: Therefore, keeping the occupancy of the hash table low is very important.

## Slide 39: Hash Collisions: Prior Works
CPU domain solution: Dynamically resizing page tables.
HPT
N
12
Notes: In the CPU domain, prior works try to reduce hash collisions by dynamically resizing the page table.

## Slide 40: Hash Collisions: Prior Works
CPU domain solution: Dynamically resizing page tables.
HPT
N
12
Notes: Along the program execution, the occupancy of the page table gradually increases.

## Slide 41: Hash Collisions: Prior Works
CPU domain solution: Dynamically resizing page tables.
HPT
N
Occupancy > Threshold
12
Notes: When the occupancy of the table reaches its threshold,

## Slide 42: Hash Collisions: Prior Works
CPU domain solution: Dynamically resizing page tables.
HPT
HPT
N
2N
Dynamic
Resizing
Occupancy > Threshold
12
Occupancy < Threshold
Notes: it dynamically resizes the page table to reduce the occupancy of the page table.

## Slide 43: Dynamic Resizing
Dynamic resizing requires complex operations and increases PTE allocation time.
HPT
HPT
N
2N
Occupancy > Threshold
13
New
Hash Func.
Occupancy < Threshold
Notes: However, these dynamic resizing

## Slide 44: Dynamic Resizing
Dynamic resizing requires complex operations and increases PTE allocation time.
HPT
HPT
N
2N
PTE migrations for Re-hashing
Occupancy > Threshold
13
New
Hash Func.
Occupancy < Threshold
Notes: requires rehashing and PTE migrations which complicate the GPU driver and increase PTE allocation time.

## Slide 45: Dynamic Resizing
Dynamic resizing requires complex operations and increases PTE allocation time.
HPT
HPT
N
2N
PTE migrations for Re-hashing
Occupancy > Threshold
13
New
Hash Func.
Can we reduce hash collisions without dynamic resizing?
Notes: Then, can we reduce hash collisions without dynamic resizing?

## Slide 46: Dynamic Resizing
Dynamic resizing requires complex operations and increases PTE allocation time.
HPT
HPT
N
2N
PTE migrations for Re-hashing
Occupancy > Threshold
13
New
Hash Func.
Can we reduce hash collisions without dynamic resizing?
→ Simply allocate a large (fixed-size) hashed page table!
Notes: The answer is “yes”, if we simply allocate a large (fixed-size) hash table.
And, fortunately, we found that it is possible for GPUs.

## Slide 47: Outline
Background
Motivation: Why HPT Is a Good Choice for GPUs?
Fixed-Size Hashed Page Table
Evaluations
Summary
Notes: Now, I’ll explain about reasons for GPU can use a large fixed-size hashed page tables.

## Slide 48: Observations
Observation 1: Unlike CPU, GPU has the cap in the number of PTEs.
Observation 2: The size of the page table is very small.
14
Notes: First is “Unlike CPU, GPU has the cap in the number of PTEs.”

## Slide 49: Page Table Management in GPUs
Unlike CPUs, GPUs do not need to maintain PTEs of swapped-out pages.
CPU Memory
CPU
Page Table
PTE 4
PTE 5
PTE 6
PTE 7
PTE 8
Page 4
Page 5
Page 6
Page 7
Storage
Page 8
15
Notes: GPU and CPU have different page table management mechanisms.

## Slide 50: Page Table Management in GPUs
Unlike CPUs, GPUs do not need to maintain PTEs of swapped-out pages.
CPU Memory
CPU
Page Table
PTE 4
PTE 5
PTE 6
PTE 7
PTE 8
Page 4
Page 5
Page 6
Storage
Page 7
Page 8
15
Notes: For example, if a page is swapped out from CPU memory to storage,

## Slide 51: Page Table Management in GPUs
Unlike CPUs, GPUs do not need to maintain PTEs of swapped-out pages.
CPU Memory
CPU
Page Table
PTE 4
PTE 5
PTE 6
PTE 7
PTE 8
Page 4
Page 5
Page 6
Storage
Page 7
Page 8
15
Notes: the CPU’s page table still needs to maintain an invalid PTE of the swapped-out page.
These invalid PTEs make it hard to predict how many PTEs will be in the page table.
Therefore, for the CPU case, we can not simply allocate a fixed-size hashed page table.

## Slide 52: Page Table Management in GPUs
Unlike CPUs, GPUs do not need to maintain PTEs of swapped-out pages.
CPU Memory
CPU
Page Table
PTE 4
PTE 5
PTE 6
PTE 7
PTE 8
Page 4
Page 5
Page 6
Storage
Page 7
Page 8
GPU Memory
GPU
Page Table
PTE 0
PTE 1
PTE 2
PTE 3
Page 0
Page 1
Page 2
Page 3
15
Notes: However, in the case of GPU,

## Slide 53: Page Table Management in GPUs
Unlike CPUs, GPUs do not need to maintain PTEs of swapped-out pages.
CPU Memory
CPU
Page Table
PTE 4
PTE 5
PTE 6
PTE 7
PTE 8
Page 4
Page 5
Page 6
Page 0
Storage
Page 7
Page 8
GPU Memory
GPU
Page Table
PTE 0
PTE 1
PTE 2
PTE 3
Page 1
Page 2
Page 3
15
Notes: if a page is swapped out from GPU memory to CPU,

## Slide 54: Page Table Management in GPUs
Unlike CPUs, GPUs do not need to maintain PTEs of swapped-out pages.
CPU Memory
CPU
Page Table
PTE 4
PTE 5
PTE 6
PTE 7
PTE 8
Page 4
Page 5
Page 6
Page 0
Storage
Page 7
Page 8
GPU Memory
GPU
Page Table
PTE 0
PTE 1
PTE 2
PTE 3
Page 1
Page 2
Page 3
15
Notes: the GPU’s page table does not need to maintain the corresponding PTE.

## Slide 55: Page Table Management in GPUs
Unlike CPUs, GPUs do not need to maintain PTEs of swapped-out pages.
CPU Memory
CPU
Page Table
PTE 0
PTE 4
PTE 5
PTE 6
PTE 7
PTE 8
Page 4
Page 5
Page 6
Page 0
Storage
Page 7
Page 8
GPU Memory
GPU
Page Table
PTE 1
PTE 2
PTE 3
Page 1
Page 2
Page 3
15
Notes: This is because CPU’s page table will maintain the PTE of swapped out page.
This is a key difference between CPU and GPU page table.

## Slide 56: Maximum Number of PTEs
We can find the maximum number of PTEs in the GPU’s local page table.
GPU Memory
GPU
Page Table
?
Page 0
Page 1
Page 2
Page 3
16
Notes: With this observation,

## Slide 57: Maximum Number of PTEs
We can find the maximum number of PTEs in the GPU’s local page table.
GPU Memory
GPU
Page Table
Max. = 4
Page 0
Page 1
Page 2
Page 3
Max. # of PTEs
16
Notes: Now we can know that the maximum number of PTEs in the GPU’s page table

## Slide 58: Maximum Number of PTEs
We can find the maximum number of PTEs in the GPU’s local page table.
GPU Memory
GPU
Page Table
Max. = 4
Page 0
Page 1
Page 2
Page 3
Max. # of PTEs
=
Max. # of pages in the GPU memory
16
Notes: is equal to the maximum number of pages in the GPU’s memory.

## Slide 59: Observations
Observation 1: Unlike CPU, GPU has the cap in the number of PTEs.
Observation 2: The size of the page table is very small.
17
Notes: The second observation is the size of page tables is very small.

## Slide 60: Fraction of Page Tables to Total Memory
The size of page tables that contains all mappings in the GPUs is only 0.2% of total memory
Total GPU Memory
18
Notes: The size of RPT that contains whole mappings in the GPU’s memory

## Slide 61: Fraction of Page Tables to Total Memory
The size of page tables that contains all mappings in the GPUs is only 0.2% of total memory
Total GPU Memory
Radix Page Tables (0.2% of total memory)
18
Notes: is only 0.2% of total GPU memory.

## Slide 62: Fraction of Page Tables to Total Memory
The size of page tables that contains all mappings in the GPUs is only 0.2% of total memory
Even if we allocate 5 times larger page tables, they only occupy 1% of the total memory.
Total GPU Memory
Radix Page Tables (0.2% of total memory)
Hashed Page Tables (1% of total memory)
18
Notes: Therefore, even if we allocate a large hashed page table to reduce hash collision, it will occupy only small portion of the total memory.
For example, if we allocate 5 times larger HPT than the RPT, it occupies only 1% of total GPU memory.

## Slide 63: Our Proposal: A Fixed-Size Hashed Page Table
Observation 1: Unlike CPU, GPU has the cap in the number of PTEs.
Observation 2: The portion of page tables is very small.
19
Notes: These two key observations

## Slide 64: Our Proposal: A Fixed-Size Hashed Page Table
Observation 1: Unlike CPU, GPU has the cap in the number of PTEs.
Observation 2: The portion of page tables is very small.
19
Using a large fixed-size hash table as a GPU’s page table!
Notes: allow us to use a large fixed-size hash table as a GPU’s page table.

## Slide 65: Our Proposal: A Fixed-Size Hashed Page Table
Observation 1: Unlike CPU, GPU has the cap in the number of PTEs.
Observation 2: The portion of page tables is very small.
19
Using a large fixed-size hash table as a GPU’s page table!
(It can fundamentally reduce hash collisions in advance)
Notes: It can fundamentally reduce hash collisions in advance without a complex dynamic resizing.

## Slide 66: A Fixed-Size Hashed Page Table
Occupancy
20
Timeline
End of
application
Threshold
(max. # of pages in GPU)
A large, fixed-size hashed page table
Notes: As a result, with the large, fixed-size hashed page table,

## Slide 67: A Fixed-Size Hashed Page Table
Occupancy
20
Timeline
End of
application
Threshold
(max. # of pages in GPU)
A large, fixed-size hashed page table
Notes: the occupancy of the page table does not exceed the pre-determined threshold

## Slide 68: A Fixed-Size Hashed Page Table
Occupancy
20
Timeline
End of
application
Threshold
(max. # of pages in GPU)
A large, fixed-size hashed page table
Notes: along the program execution, preventing frequent hash collisions.

## Slide 69: Outline
Background
Motivation
Fixed-Size Hashed Page Table
Evaluations
Summary
Notes: Next, I’ll explain about our proposed architecture, a Fixed-Size Hashed Page Table.

## Slide 70: Architectural Overview
21
Step Table
Victim Buffer
Hashed Page Table
(Fixed and Large Size)
Step Cache
Device Memory
GMMU
Page Table Walkers
Remote PTE LRU Policy
GPU Driver
Notes: This is a simple architectural overview.

## Slide 71: Architectural Overview
21
Step Table
Victim Buffer
Hashed Page Table
(Fixed and Large Size)
Step Cache
Device Memory
GMMU
Page Table Walkers
Remote PTE LRU Policy
GPU Driver
Notes: We allocate a large fixed-size hashed page table in the device memory, thereby reducing hash collisions without dynamic resizing.

## Slide 72: Challenges
Challenge 1: Hash Collision Handling
Challenge 2: Remote Mapping Management
22
Notes: However, there are remaining design challenges.

## Slide 73: Challenges
Challenge 1: Hash Collision Handling
Challenge 2: Remote Mapping Management
22
Notes: First is hash collision handling.
Even if there are few hash collisions due to large hash table, there remains the probability to occur hash collisions.

## Slide 74: Challenges
Challenge 1: Hash Collision Handling
Challenge 2: Remote Mapping Management
Open-Addressing with a Step Table
22
Notes: To resolve hash collisions effectively, we introduce open addressing with a Step Table.

## Slide 75: A Fixed-Size Hashed Page Table
23
Step Table
Victim Buffer
Hashed Page Table
(Fixed and Large Size)
Step Cache
Device Memory
GMMU
GPU Driver
Page Table Walkers
Open Addressing
Remote PTE LRU Policy
Notes: When allocating PTEs, if there is hash collision, the GPU driver resolves it using a simple open-addressing scheme.

## Slide 76: Open-Addressing
Hash collision handling using an open-addressing scheme.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
24
Notes: This is a simple example of allocating and access PTE.

## Slide 77: Open-Addressing
Hash collision handling using an open-addressing scheme.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
24
Notes: First, the GPU driver access HPT with the hash value of given VA.

## Slide 78: Open-Addressing
Hash collision handling using an open-addressing scheme.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
24
Notes: After accessing HPT, the GPU driver compares tag values to validate if a hash collision occurs.
In this example, hash collisions occurs because tags are mismatched.

## Slide 79: Open-Addressing
Hash collision handling using an open-addressing scheme.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
Open addressing
Step++
24
Notes: In that case, open-addressing scheme resolves hash collisions by probing next entry.

## Slide 80: Open-Addressing
Hash collision handling using an open-addressing scheme.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
Open addressing
Step++
Step++
24
Notes: It probes iteratively until it finds a matching entry or an empty entry.

## Slide 81: Open-Addressing
Hash collision handling using an open-addressing scheme.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
Open addressing
Step++
Step++
0x0A
0xCC
Allocate
New PTE
23
Notes: In this example, since it finds an empty entry, the driver allocates new PTE in that slot.

## Slide 82: A Fixed-Size Hashed Page Table
22
Step Table
Victim Buffer
Hashed Page Table
(Fixed and Large Size)
Step Cache
Device Memory
GMMU
GPU Driver
Page Table Walkers
Open Addressing
Remote PTE LRU Policy
Notes: At the PTE access time, we needs a sequential memory access again to find a tag matching entry with the open-addressing scheme.
To remove this sequential probing overhead at the PTE access, we introduce a Step Table.
Step Table can simply remove additional memory access of open-addressing probing sequences.

## Slide 83: Step Table
Step Table stores open-addressing “Step” value.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
Step++
Step++
0x0A
0xCC
Allocate
New PTE
Step Table
0x02
Tag
•••
Step
0
0x1E
1
Empty
Empty
0x0A
2
Fill Step Table
24
Notes: At the PTE allocation time, the driver stores an open-addressing “Step” value in the Step Table.
In this example, the Step value is two.

## Slide 84: Step Table
Step Table stores open-addressing “Step” value.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
Step++
Step++
0x0A
0xCC
Allocate
New PTE
Step Table
0x02
Tag
•••
Step
0
0x1E
1
Empty
Empty
0x0A
2
Fill Step Table
24
Access without sequential probing
Notes: With the stored “Step” value, at the PTE access time, the page table walker can directly access precise PTE without sequentially probing the page table.

## Slide 85: A Fixed-Size Hashed Page Table
25
Step Table
Victim Buffer
Hashed Page Table
(Fixed and Large Size)
Step Cache
Remote PTE LRU Policy
Device Memory
GMMU
GPU Driver
Page Table Walkers
Open Addressing
Notes: However, accessing Step Table can introduce another memory access.
To mitigate this overhead, we introduce a Step Cache in the GPU MMU.

## Slide 86: Step Cache
Step Cache allows page table walkers to skip accessing Step Table.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
Step++
Step++
0x0A
0xCC
Allocate
New PTE
Step Table
0x02
Tag
•••
Step
0
0x1E
1
Empty
Empty
0x0A
2
Fill Step Table
26
Access without sequential probing
Notes: Step Cache stores the recently accessed “Step” value.
So, it allows the page table walker

## Slide 87: Step Cache
Step Cache allows page table walkers to skip accessing Step Table.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
Step++
Step++
0x0A
0xCC
Allocate
New PTE
Step Table
0x02
Tag
•••
Step
0
0x1E
1
Empty
Empty
0x0A
2
Fill Step Table
26
Access without sequential probing
Skip
Notes: to skip accessing Step Table at the PTE access time.

## Slide 88: Step Cache
Step Cache allows page table walkers to skip accessing Step Table.
Page offset
0x0A
H
+
VA
HPT
0x02
Tag
•••
PTE
0xAA
0x1E
0xBB
Empty
VPN tag
Empty
PTBR
Hash collision!
Step++
Step++
0x0A
0xCC
Allocate
New PTE
Step Table
0x02
Tag
•••
Step
0
0x1E
1
Empty
Empty
0x0A
2
Fill Step Table
26
Access without sequential probing
Skip
≈ 100% hit rate
Notes: Also, since Step Cache has higher bit density than PWC, it shows 100% hit rate with the same area overhead.
With this design, we can get the desired PTE with only one memory access.

## Slide 89: Challenges
Challenge 1: Hash Collision Handling
Challenge 2: Remote Mapping Management
Open-Addressing with a Step Table
27
Notes: Next challenge is remote mapping management.

## Slide 90: Remote Access in GPUs
GPU can access remote data by maintaining remote PTEs in the page table.
28
PCIe
CPU Memory
GPU Memory
Page 0
Remote access
Notes: Conventional GPUs support remote access to other devices memory without copying or migrating data to GPU’s memory.
This allows GPU to manage external bandwidth efficiently.

## Slide 91: Remote Access in GPUs
GPU can access remote data by maintaining remote PTEs in the page table.
28
PCIe
CPU Memory
GPU Memory
Page 0
Remote access
GPU
Page Table
PTE 0
Notes: However, to do remote access, the GPU’s page table needs to maintain remote mappings in it.

## Slide 92: Remote Access in GPUs
GPU can access remote data by maintaining remote PTEs in the page table.
28
PCIe
CPU Memory
GPU Memory
Page 0
Remote access
GPU
Page Table
PTE 0
Remote mappings can increase hash collisions!
Notes: These remote mappings increase the occupancy of the page table causing more hash collisions.

## Slide 93: Challenges
Challenge 1: Hash Collision Handling
Challenge 2: Remote Mapping Management
Open-Addressing with a Step Table
Remote PTE Replacement Policy and a Victim Buffer
29
Notes: To address this challenge, we introduce remote PTE replacement policy with a Victim Buffer.

## Slide 94: A Fixed-Size Hashed Page Table
30
Step Table
Victim Buffer
Hashed Page Table
(Fixed and Large Size)
Step Cache
Remote PTE LRU Policy
Device Memory
GMMU
GPU Driver
Page Table Walkers
Open Addressing
Notes: GPU driver evict remote mappings using the LRU counter.

## Slide 95: Remote PTE Eviction Policy
GPU driver evicts dead remote PTEs from the page table using LRU policy.
PTE 3
PTE 0
PTE 1
PTE 2
Evict
Remote PTE Eviction Policy
LRU
MRU
31
HPT
Threshold
Victim Buffer
Notes: If the occupancy of the GPU’s page table reaches its threshold due to remote mappings,

## Slide 96: Remote PTE Eviction Policy
GPU driver evicts dead remote PTEs from the page table using LRU policy.
PTE 3
PTE 0
PTE 1
PTE 2
Evict
Remote PTE Eviction Policy
LRU
MRU
31
HPT
Threshold
Victim Buffer
Notes: If the occupancy of the GPU’s page table reaches its threshold due to remote mappings,

## Slide 97: Remote PTE Eviction Policy
GPU driver evicts dead remote PTEs from the page table using LRU policy.
PTE 3
PTE 0
PTE 1
PTE 2
Evict
Remote PTE Eviction Policy
LRU
MRU
31
HPT
Threshold
Victim Buffer
Victim
Notes: The GPU driver evicts the remote mapping at the LRU position.

## Slide 98: A Fixed-Size Hashed Page Table
32
Step Table
Victim Buffer
Hashed Page Table
(Fixed and Large Size)
Step Cache
Remote PTE LRU Policy
Device Memory
GMMU
GPU Driver
Page Table Walkers
Open Addressing
Notes: The evicted mappings are maintained in the Victim Buffer.

## Slide 99: Victim Buffer
Victim Buffer prevents page fault handling for re-accessed evicted entries.
PTE 3
PTE 0
PTE 1
PTE 2
Evict
Remote PTE Eviction Policy
LRU
MRU
33
HPT
Threshold
Victim Buffer
Evict!
Victim
Notes: The Victim Buffer prevents page fault handling for re-accessed evicted entries.

## Slide 100: Victim Buffer
Victim Buffer prevents page fault handling for re-accessed evicted entries.
PTE 3
PTE 0
PTE 1
PTE 2
Evict
Remote PTE Eviction Policy
LRU
MRU
33
HPT
Threshold
Victim Buffer
Evict!
Victim
More details are in our paper!
Notes: For more details, please refer to our paper.

## Slide 101: Outline
Background
Motivation
Fixed-Size Hashed Page Table
Evaluations
Summary
Notes: Next is our evaluations.

## Slide 102: Methodology
Simulator: GPGPU Sim v4.0
  Shared L2 TLB: 1024 entries
  Page table walkers: 16
  Page walk caches: 32 entries per level
  Page table size: 0.5% of working set size
Page table walk sensitive and agnostic workloads.
34
Notes: We evaluate our architecture using GPGPU-Sim extended with virtual memory systems.

## Slide 103: Performance Improvement
For irregular GPU applications, Fixed-Size Hashed Page Table outperforms RPTs by 27.8% on average.
Chart: Speedup
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
RPT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FS-HPT | 1.3547 | 1.2658 | 1.3493 | 1.3197 | 1.158 | 1.3582 | 1.1827 | 1.2572 | 1.2785 | 0.99839 | 1.001 | 0.99897 | 1.0334 | 1.0191 | 1 | 0.99984 | 1 | 1.0063
Ideal PWC | 1.3826 | 1.2913 | 1.3609 | 1.3338 | 1.1638 | 1.3678 | 1.1857 | 1.2604 | 1.2908 | 0.99839 | 1.0029 | 0.99935 | 1.0334 | 1.0203 | 1 | 1.0013 | 0.99949 | 1.0068
35
HPT
Notes: For irregular GPU applications, the Fixed-Size HPT outperforms RPTs by 27.8% on average.

## Slide 104: Performance Improvement
For irregular GPU applications, Fixed-Size Hashed Page Table outperforms RPTs by 27.8% on average.
Chart: Speedup
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
RPT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FS-HPT | 1.3547 | 1.2658 | 1.3493 | 1.3197 | 1.158 | 1.3582 | 1.1827 | 1.2572 | 1.2785 | 0.99839 | 1.001 | 0.99897 | 1.0334 | 1.0191 | 1 | 0.99984 | 1 | 1.0063
Ideal PWC | 1.3826 | 1.2913 | 1.3609 | 1.3338 | 1.1638 | 1.3678 | 1.1857 | 1.2604 | 1.2908 | 0.99839 | 1.0029 | 0.99935 | 1.0334 | 1.0203 | 1 | 1.0013 | 0.99949 | 1.0068
27.8%
35
HPT
Notes: For irregular GPU applications, the Fixed-Size HPT outperforms RPTs by 27.8% on average.

## Slide 105: Performance Improvement
For irregular GPU applications, Fixed-Size Hashed Page Table outperforms RPTs by 27.8% on average.
Chart: Speedup
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
RPT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FS-HPT | 1.3547 | 1.2658 | 1.3493 | 1.3197 | 1.158 | 1.3582 | 1.1827 | 1.2572 | 1.2785 | 0.99839 | 1.001 | 0.99897 | 1.0334 | 1.0191 | 1 | 0.99984 | 1 | 1.0063
Ideal PWC | 1.3826 | 1.2913 | 1.3609 | 1.3338 | 1.1638 | 1.3678 | 1.1857 | 1.2604 | 1.2908 | 0.99839 | 1.0029 | 0.99935 | 1.0334 | 1.0203 | 1 | 1.0013 | 0.99949 | 1.0068
27.8%
Achieves nearly one memory access per PTW
2. Achieves 22% reduction in PTW latency
35
HPT
Notes: This is because our proposed architecture requires only one memory access per page table walk, reducing PTW latency by 22%.

## Slide 106: Outline
Background
Motivation
Fixed-Size Hashed Page Table
Evaluations
Summary
Notes: Let me wrap up my presentation.

## Slide 107: Summary
Fixed-Size Hashed Page Table proposes an HPT design dedicated to GPUs.
  Use a large fixed-size hashed page table (no need for dynamic resizing).
  Open-addressing with a Step Table effectively resolves hash collisions.
  Victim Buffer manages remote mappings.
36
Notes: Fixed-Size Hashed Page Table proposes an HPT design dedicated for GPUs.

## Slide 108: Summary
Fixed-Size Hashed Page Table proposes an HPT design dedicated to GPUs.
  Use a large fixed-size hashed page table (no need for dynamic resizing).
  Open-addressing with a Step Table effectively resolves hash collisions.
  Victim Buffer manages remote mappings.
To the best of our knowledge, Fixed-Size Hashed Page Table is the first work to apply Hashed Page Tables in GPUs.
36
Notes: To the best of our knowledge, this is the first work to apply Hashed Page Tables in GPUs.

## Slide 109: Summary
Fixed-Size Hashed Page Table proposes an HPT design dedicated to GPUs.
  Use a large fixed-size hashed page table (no need for dynamic resizing).
  Open-addressing with a Step Table effectively resolves hash collisions.
  Victim Buffer manages remote mappings.
To the best of our knowledge, Fixed-Size Hashed Page Table is the first work to apply Hashed Page Tables in GPUs.
Our proposed technique shows a substantial performance improvement (27.8%) by effectively reducing address translation overhead.
36
Notes: Our proposed architecture shows a substantial performance improvement by effectively reducing address translation overhead, especially for page table walks.

## Slide 110: Rethinking Page Table Structure for Fast Address Translation in GPUs: A Fixed-Size Hashed Page Table
Sungbin Jang, Junhyeok Park, Osang Kwon, Yongho Lee, and Seokin Hong
Sungkyunkwan University
sunbi3361@skku.edu
PACT '24: International Conference on Parallel Architectures and Compilation Techniques
Notes: Thank you for listening.
Feel free to ask any questions.

## Slide 111: Backup Slides
Notes: Good morning, I’m a Ph.D. student at Sungkyunkwan University, advised by Professor Seokin Hong.
Now, I’ll talk about our holistic research paper, Rethinking Page Table Structure for Fast Address Translation in GPUs: A Fixed-Size Hashed Page Table.

## Slide 112: Compatibility with Prior Work
Fixed-Size Hashed Page Tables can be orthogonally applicable with other prior works well.
Chart: Speedup
| ATX | GEV | MVT | SYK | BC | BFS | SP | NW | Avg. | 2DC | BIC | COR | CC | KC | HOT | PF | LU | Avg. | Irregular | Regular
RPT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RPT+NHA | 0.99445 | 0.99273 | 1.0084 | 1.5685 | 1.1541 | 1.3534 | 1.4764 | 1.1316 | 1.2099 | 0.99957 | 0.99085 | 1 | 1.9502 | 1.4492 | 1.0015 | 1 | 0.99465 | 1.1732
FS-HPT | 1.3547 | 1.2658 | 1.3493 | 1.3197 | 1.158 | 1.3582 | 1.1827 | 1.2572 | 1.2807 | 0.99839 | 1.001 | 1.0153 | 1.0334 | 1.0191 | 1 | 0.99984 | 1 | 1.0084
FS-HPT+NHA | 1.3542 | 1.2658 | 1.3682 | 2.308 | 1.4211 | 1.8815 | 1.8769 | 1.4632 | 1.6174 | 0.99839 | 1.001 | 1.0153 | 2.0065 | 1.4801 | 1.002 | 1.0001 | 1.0127 | 1.1895
Ideal PWC+NHA | 1.3761 | 1.2871 | 1.3682 | 2.3182 | 1.4394 | 1.9213 | 1.8797 | 1.4889 | 1.6348 | 0.99839 | 1.001 | 1.0153 | 2.0454 | 1.4916 | 1.002 | 1.0001 | 1.0161 | 1.1962
61.7%